## Slide 1: Implementing IPv6
Introducing IPv6

## Slide 2: IPv6: Larger Address Space
IPv4
  32 bits or 4 bytes long
    4,200,000,000 possible addressable nodes
IPv6
  128 bits or 16 bytes: four times the bits of IPv4
    3.4 * 1038 possible addressable nodes
    340,282,366,920,938,463,374,607,432,768,211,456
    5 * 1028 addresses per person
~ =
~ =
~ =
~ =

## Slide 3: IPv6: Address Representation (Hexadecimal)

## Slide 4
Decimal | Hexadecimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111

## Slide 5: IPv6: Address Representation
2001:0ABC:00AB:000A:0000:0000:0000:1001
2001:0ABC:00AB:000A:0000:0000:0000:1001
2001:ABC:AB:A:0:0:0:1001
2001:ABC:AB:A::1001

## Slide 6: IPv6: Address Scheme

## Slide 7: IPv6: Global Unicast Address (2000::/3)
2001:0000:0000:0001:: /64
2001:0000:0000:0002:: /64
2001:0000:0000:0003:: /64
2001:0000:0000:XXXX:: /64
2001:0000:0000::/48
Internet Network
2001:0000:0000::/48
2001:0:0:0002:: /64
2001:0:0:0001:: /64
2001:0:0:0003:: /64

## Slide 8: IPv6: Address Type
IPv6 does not have a Broadcast Address

## Slide 9: IPv6: Multicast Address

## Slide 10: IPv6: Link-Local Address
PC1
F0/0
F0/1
FE80::1
FE80::1
FE80::0200:AAFF:FEAA:1001
FE80::020C:42FF:FE28:7945
PC2
interface f0/0
ipv6 address fe80::1 link-local
2001:0:0:1::1/64
2001:0:0:2::2/64
Router(config)# interface f0/0
Router(config-if)# ipv6 enable
Router# show ipv6 interface brief
FastEthernet0/0 [up/up]
fe80::a8bb:ccff:fe00:4001
Router(config)# ipv6 unicast-routing
Router(config)# interface f0/0
Router(config-if)# ipv6 address 2001:0:0:1::2/64
Router(config-if)# ipv6 address 2001:0:0:1:: /64 eui-64

## Slide 11: IPv6: Multicast Address

## Slide 12: IPv6: Link-Local Address
PC1

## Slide 13: IPv6: Configuring Address

## Slide 14: IPv6: Configuring Address

## Slide 15: IPv6: Configuring Address
PC1
C:\> netsh interface ipv6 install
C:\> netsh
netsh> interface ipv6
netsh interface ipv6> add address “Realtek” 2009::1
netsh interface ipv6> add address “Realtek” 2009::2
netsh interface ipv6> add address “Realtek” 200A::2
netsh interface ipv6> delete address “Realtek” 2009::1
netsh interface ipv6> show address
C:\> ping ::1

## Slide 16: IPv6: Configuring Address
VPC
VPCS> ip 2001:1::2
PC1 : 2001:1::2/64
VPCS> show ipv6
NAME : VPCS[1]
LINK-LOCAL SCOPE : fe80::250:79ff:fe66:6805/64
GLOBAL SCOPE : 2001:1::2/64
…

## Slide 17: IPv6: SLAAC (Stateless Address AutoConfiguration)
IPv4
IPv6
IPv4 Internet
IPv6 Internet
ipv6 unicast-routing
interface g1
ip address 10.0.0.1 255.255.255.0
ipv6 address 2001::1/64
ipv6 address 2002::1/64
ipv6 nd ra interval 200
Router Advertisement:
2001::/64
2002::/64
MAC 0000.AAAA.1002
2001::0200:AAFF:FEAA:1002/64
2002::0200:AAFF:FEAA:1002/64
Dual-Stack
Link-local

## Slide 18: IPv6: SLAAC (Stateless Address AutoConfiguration)
IPv4 Internet
IPv6 Internet
Dual-Stack

## Slide 19: IPv6: Stateful DHCP
ipv6 dhcp pool IPV6_DHCPPOOL
address prefix 2001::/64 lifetime infinite infinite
link-address 2001::1/64
dns-server 2001::1
domain-name cisco.com
DHCP
Server
g1
2001::1
int g1
ipv6 address 2001::1/64
ipv6 enable
ipv6 nd ra suppress
ipv6 dhcp server IPV6_DHCPPOOL
int g1
ipv6 address dhcp
ipv6 enable
DHCP
Client

## Slide 20: Stateless Address AutoConfiguration
Server
Client
2001::1/64
ipv6 address autoconfig
int f0/0
ipv6 nd prefix 2001::/64 600 300 no-autoconfig
Valid Lifetime
Preferred Lifetime
ipv6 unicast-routing
int f0/0
ipv6 nd ra interval 4
Router Advertisement
4s

## Slide 21: Stateless Address AutoConfiguration
Server# show ipv6 interface g1
GigabitEthernet1 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::20C:29FF:FE1F:14BB
No Virtual link-local address(es):
No global unicast address is configured
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF1F:14BB
MTU is 1500 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds (using 30000)
ND advertised reachable time is 0 (unspecified)
ND advertised retransmit interval is 0 (unspecified)
ND router advertisements are sent every 200 seconds
ND router advertisements live for 1800 seconds
ND advertised default router preference is Medium
Hosts use stateless autoconfig for addresses.
Server#

## Slide 22
ipv6 dhcp pool IPV6_DHCPPOOL
dns-server 2001::1
domain-name cisco.com
DHCP
Server
Stateless DHCP
g1
2001::1
int g1
ipv6 address 2001::1/64
ipv6 enable
ipv6 nd other-config-flag
ipv6 dhcp server IPV6_DHCPPOOL
int g1
ipv6 address autoconfig
ipv6 enable
DHCP
Client

## Slide 23: EUI-64 to IPv6 Interface Identifier (Cont.)
  A modified EUI-64 address is formed by inserting “FFFE” and “complementing” a bit identifying the uniqueness of the MAC address.
Notes: EUI-64 to IPv6 Interface Identifier
The interface identifier for stateless auto-configuration in an Ethernet environment uses the modified EUI-64 format. This format expands the 48-bit Ethernet MAC address format to a 64-bit version by inserting "FFFE" in the middle of the 48 bits. This creates a 64-bit version.
The 7th bit (starting with the leftmost bit as “1”) in an IPv6 interface identifier is referred to as the Universal/Local bit, or U/L bit. This bit identifies whether this interface identifier is locally unique on the link or that it is universally unique. In the case where the interface identifier is created from an Ethernet MAC address, it is assumed that the MAC address is universally unique and, therefore, the interface identifier is universally unique.
The rationale of the U/L bit is for future use of the upper-layer protocols to uniquely identify a connection, even in the context of a change in the leftmost part of the address. However, this is not yet used.
The 8th bit (starting with leftmost bit as “1”), also known as the “G” bit, is a group/individual bit for managing groups.
Note to Graphic Designer:
Animation is needed for this slide.
Stage 1: Show Ethernet MAC address (top address on slide) and two FF and FE blocks.
Stage 2: Show the FF and FE blocks going in-between blocks 27 and 17 of Ethernet address. Change label of address to Ethernet MAC address (64 bits). Also Show the U/L bit coming out of the OO block with the where U = information.
Stage 3: Show final Modified EUI-64 address.
Instructor Note
Discuss the transformative process for EUI-64 to IPv6 interface identifier.

## Slide 24: EUI-64 to IPv6 Interface Identifier (Cont.)
  A modified EUI-64 address is formed by inserting “FFFE” and “complementing” a bit identifying the uniqueness of the MAC address.
Notes: EUI-64 to IPv6 Interface Identifier
The interface identifier for stateless auto-configuration in an Ethernet environment uses the modified EUI-64 format. This format expands the 48-bit Ethernet MAC address format to a 64-bit version by inserting "FFFE" in the middle of the 48 bits. This creates a 64-bit version.
The 7th bit (starting with the leftmost bit as “1”) in an IPv6 interface identifier is referred to as the Universal/Local bit, or U/L bit. This bit identifies whether this interface identifier is locally unique on the link or that it is universally unique. In the case where the interface identifier is created from an Ethernet MAC address, it is assumed that the MAC address is universally unique and, therefore, the interface identifier is universally unique.
The rationale of the U/L bit is for future use of the upper-layer protocols to uniquely identify a connection, even in the context of a change in the leftmost part of the address. However, this is not yet used.
The 8th bit (starting with leftmost bit as “1”), also known as the “G” bit, is a group/individual bit for managing groups.
Note to Graphic Designer:
Animation is needed for this slide.
Stage 1: Show Ethernet MAC address (top address on slide) and two FF and FE blocks.
Stage 2: Show the FF and FE blocks going in-between blocks 27 and 17 of Ethernet address. Change label of address to Ethernet MAC address (64 bits). Also Show the U/L bit coming out of the OO block with the where U = information.
Stage 3: Show final Modified EUI-64 address.
Instructor Note
Discuss the transformative process for EUI-64 to IPv6 interface identifier.

## Slide 25: EUI-64 to IPv6 Interface Identifier
A modified EUI-64 address is formed by inserting “FFFE” and “complementing” a bit identifying the uniqueness of the MAC address.
Notes: EUI-64 to IPv6 Interface Identifier
The interface identifier for stateless auto-configuration in an Ethernet environment uses the modified EUI-64 format. This format expands the 48-bit Ethernet MAC address format to a 64-bit version by inserting "FFFE" in the middle of the 48 bits. This creates a 64-bit version.
The 7th bit (starting with the leftmost bit as “1”) in an IPv6 interface identifier is referred to as the Universal/Local bit, or U/L bit. This bit identifies whether this interface identifier is locally unique on the link or that it is universally unique. In the case where the interface identifier is created from an Ethernet MAC address, it is assumed that the MAC address is universally unique and, therefore, the interface identifier is universally unique.
The rationale of the U/L bit is for future use of the upper-layer protocols to uniquely identify a connection, even in the context of a change in the leftmost part of the address. However, this is not yet used.
The 8th bit (starting with leftmost bit as “1”), also known as the “G” bit, is a group/individual bit for managing groups.
Note to Graphic Designer:
Animation is needed for this slide.
Stage 1: Show Ethernet MAC address (top address on slide) and two FF and FE blocks.
Stage 2: Show the FF and FE blocks going in-between blocks 27 and 17 of Ethernet address. Change label of address to Ethernet MAC address (64 bits). Also Show the U/L bit coming out of the OO block with the where U = information.
Stage 3: Show final Modified EUI-64 address.
Instructor Note
Discuss the transformative process for EUI-64 to IPv6 interface identifier.

## Slide 28
  FF01 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0001
  FF01 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0001
  0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0001
  FF01 : 0000 : 0000 : 0000 : 0000 : 0000 : 000:: 0001
  0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000
  FF01 : 0000 : 0000 : 0000 : 0000 : 0000 : 000:: 0000
  255.255.255.255
  127.0.0.1
  FF02 : : 5
  FF02 : : 6
  FF02 : : A
  224.0.0.5
  224.0.0.6
  224.0.0.10

## Slide 29: Examples of Permanent Multicast Addresses

## Slide 30
Address Types
Unicast |  | Multicast | Anycast
global | 2000::/3 | FF00::/8 | One-to-nearest
site-local | FEC0::/10 |  | devices share the address
link-local | FE80::/10 |  | provide uniform service
R1
R2
e0/1
e0/1
2001::8/64
DNS1
DNS2
interface e0/0
ipv6 address 2001::/64 anycast
interface e0/0
ipv6 address 2001::/64 anycast
2001::8/64
https://www.youtube.com/watch?v=5nC2G58qo_s

## Slide 31: Site-Local Addresses
(proposal remove by IETF)
48 bits.
16 bits SLA
Interface ID.
1111 1110 11
FEC0::/10
10 bits
128 bits
64 bits

## Slide 32: Link-Local Addresses
Link-local addresses are used for automatic address configuration, neighbor discovery, router discovery.
Link-local addresses are also used by many routing protocols.

## Slide 33: Multicast Addresses
50 bits
Interface ID
1111 1111
FF00::/8
8 bits
128 bits
64 bits
8 bits
lifetime
scope
4 bits
4 bits
0 if permanent
1 if temporary
1 = node
2 = link
5 = site
8 = organization
E = global
lifetime =
scope =

## Slide 34
Site-leve Aggregator
SLA

## Slide 35
Aggregation
  Efficient and scalable routing
2001:0410:0002:0001:BECF:00FF:FE0B:000C/64

## Slide 36: IPv6 Packet Header
Data Portion.
Version.
Traffic Class.
Flow Label.
Payload Length.
Next Header.
Hop Limit.
Source Address.
Destination Address.
32 bits

## Slide 37: IPv6: Routing
    Static
    RIPng – Next Generation
    OSPFv3
    EIGRP for IPv6

## Slide 38: IPv6: Routing
2002::/64
2001::2
ipv6 route 2002::/64 2001::2
R# show ipv6 route
S 2002::/64 [1/0] via 2001::2
ping 2002::2%GigabitEthernet1
g1
ipv6 router eigrp 100
eigrp router-id 0.0.0.2
no shutdown
interface g2
ipv6 eigrp 100
g2
ipv6 router ospf 1
router-id 1.1.1.1
interface g2
ipv6 ospf 1 area 0
show ipv6 eigrp neighbors
show ipv6 ospf neighbors
ipv6 router rip tag1
interface g2
ipv6 rip tag1 enable

## Slide 39: IPv6: IPv4-to-IPv6 Transition
    Different transition mechanisms are available:
      Dual stack
      Manual tunnel
      6to4 tunnel
      ISATAP tunnel
      Teredo tunnel
IPv6
IPv6

## Slide 40: IPv6: NAT-PT (Proxying & Translation)
Web
Server
Proxy
NAT-PT
ipv4
ipv4
ipv6
google.com
DNS: IPv6 Proxy